## Slide 1
Problem Description/Data/Reference: Final Project (RTA) - SPE 114947 (Ilk)
Problem Description:
Elements:
This is a production analysis with variable rate + changing flowing bottom hole pressure (FBHP)
This is a gas well with finite conductivity fracture (bilinear flow).
Require the use of material balance pseudo time
Require the use of pseudo-pressure integration
Challenges:
Need to guess initial gas-in-place (IGIP) and compute average reservoir pressure, pseudo time , and material balance pseudo time , using SPE 17708.
Need to plot flowing material balance equation, correct for the transient flow production and iterate for initial gas-in-place (IGIP), using the procedure in SPE 17708.
Need to use ‘De-superposition technique to incorporate finite conductivity element from Lee-Brockenbrough trilinear flow model into Ozkan’s fracture well solution. Then use the convolution theorem to convert it to the rate solution to obtain Pratikno’s type curve.
Results from publication/reference:
The time-rate-pressure for the entire history is given
The preliminary analysis is provided in SPE 84287.
The permeability and fracture half-length are obtained previously from pressure build up test (PBU)
Data Description:
There are 5,039 data points with noise.
Need to manually clean the data and take out some outliers from the shut-in events. The edited data set has only 4,416 data point.
Reference:
Pratikno, H., Rushing, J. A., and Blasingame, T. A. (2003) Decline Curve Analysis Using Type Curves - Fractured Wells. Society of Petroleum Engineers. doi:10.2118/84287-MS
Table of Properties
Fluid Properties:
REF. GAS FVF, MSCF/STB = 0.5483
REF. GAS VISCOSITY, cp = 0.03605
REF. TOTAL COMPRESSIBILITY, 1/psia = 5.0975E-5
TEMPERATURE, deg F = 300
Reservoir Properties:
RESERVOIR THICKNESS, ft = 170
WELLBORE RADIUS, ft = 0.333
POROSITY, fraction = 0.088
EQUIVALENT POROSITY, fraction = 0.07647 (*)
(*) Adjusted to the irreducible water saturation
Swi = 0.131
Production Properties:
INITIAL PRESSURE (Pi), psia = 9330
PSEUDO INITIAL PRESSURE (Ppi),psia = 7540.13
INITIAL GAS-IN-PLACE (G), BSCF = 3.23 (*)
(*) INTIAL GUESS FROM SPE 17708 METHOD
Properties to be Solved: (Final Estimates)
(from Python Program)
(Finite-conductivity fracture in a bounded
reservoir model)
PERMEABILITY (k), md = 0.016
FRACTURE HALF-LENGTH (xf), ft = 112
EQUIVALENT SKIN (S), Dim-Less = -5.12 (*)
FRACTURE COND.(FcD), Dim-less = 27
RESERVOIR RADIUS (re), ft = 491
INITIAL GAS-IN-PLACE (G), BSCF = 3.20 (**)
(*) Calculated from S = -ln(xf/2rw)
(**) Use volumetric calculation from reservoir properties and matched reservoir radius (re)

## Slide 2
Diagnostic Plot [log-log]:
Workflow Plot (SPE 17708 - Blasingame):
Estimate (guess) initial gas-in-place (G)
Calculate average reservoir pressure, using the material balance equation. For Gp, use the trapezoid rule of qg. Note that z-factor is in a function of reservoir pressure
3) Calculate pseudo time based on
4) Calculate material balance pseudo time as follows;
5) Calculate pseudo-pressure as follows;
6) Plot the flowing material balance equation (between rate-normalized pseudo-pressure and material balance pseudo time to obtain initial gas-in-place and the reciprocal of productivity index from slope and intercept, respectively.
7) Need to correct extra production from a transient flow
Material Balance Pseudo Time and Initial Gas-In-Place Iterations (G)
Calculations:
Estimate IGIP = 3.23 BSCG
Estimate productivity index =
1 / 2.5559 = 0.391 psi / (MSCF/D)
3) IGIP is sensitive to curve-fitting, depending on how the time to stabilized flow is selected. I will cross-check this IGIP with the one obtained from RTA type curve matching

## Slide 3
Analysis Summary Plots (Model)
“Model” matching: (by Python)
Excellent match throughout history!
qDdid is off a bit toward the beginning
(numerical artifact)
Using Pratikno TC
Excellent overlay on TC
b = 1 (MB. Time)
Finite conductivity
Excellent match throughout history!
Type curve matching results:
Calculation check for IGIP:
This result agrees well with G obtained from pseudo time calculation, using the method in SPE 17708 (3.23 BSCF)

## Slide 4
Challenge & Issues:
[De-superposition] Blasingame and Poe added “Finite-conductivity” element of trilinear solution to Okzan’s solution which includes the pseudo radial flow at the late time. Use and
Method of Work / Discussion of Results
Method of Work:
Starting Point:
Type curve matching requires Stehfest’s algorithm.
Need to follow IGIP and calculation shown in slide 2
Governing Equations:
Discussion of Results:
Diagnostics:
The bilinear flow at early time is clear. The function in the transient stem has slope of ¼.
The depletion stem follows the harmonic solution because the material balance pseudo time is used.
Excellent match on qDd and qDdi
Some numerical artifact in qDdid toward the beginning
Analyses:
Permeability from RTA is identical to the one from PTA (k = 0.016 md).
Fracture half-length from RTA (xf = 112 ft) agrees extremely well with the one from PTA (xf = 119 ft)
The well is stimulated (negative skin = -5.12)
According to RTA, fracture is finite fracture-conductive (FcD = 27) In PTA, FcD = 4. Bilinear flow regime is more pronounced in PBU.
Gas in-place estimates from SPE 17708 iteration and type curve match agree within 0.03 BSCF.
Assessment:
Use L = 0.1-0.15 to smooth the data provides even better-quality rate-integral derivative (qDdid)
Recommendations/Extra work:
Technical developments that would help?
The augmented plot for -derivative
Try log-log plot by ‘flipping’ TC upside down and work with “rate-normalized pressure (RNP)” instead of “pressure-normalized rate (PNR)”
The vs plot or “Bi-linear flow” specialized plot could yield the straight-line in case of finite-conductivity fracture.
Blasingame-Poe Desuperposition “Trilinear Pseudo radial” | 
Lee-Brockenbrough Trilinear flow equation | 
Infinite Cond. Fracture soln. (Okzan/Laplace) | 
Correlation | (check SPE 84287 Eq.5)
Dimensionless rate from and | 
Dimensionless decline function | 
Dimensionless decline material balance pseudo time | 
Blasingame-Poe Desuperposition “Trilinear Pseudo radial” | 
Lee-Brockenbrough Trilinear flow equation | 
Infinite Cond. Fracture soln. (Okzan/Laplace) | 
Dimensionless decline function | 
Dimensionless decline material balance pseudo time |